## Slide 1: Evaluation of a Wind Energy Harvesting Concept for Plug In Hybrid and Electric Vehicles
Maharshi Patel
Department of Mechanical and Mechatronics Engineering
University of Waterloo
Waterloo, Ontario, Canada
Friday, August 28, 2015
Waterloo, Ontario, Canada

## Slide 2: Acknowledgements
Prof. Kaan Inal
Christopher Kohar

## Slide 3: Contents
Abbreviations
Introduction
  Re-cap
    Problem
    Solution
    Feasibility test
Literature Review
  BEM – Theory
CFD ANSYS
  Fluid Theory
  Turbulence Theory
  Model
    Geometry
    Mesh
    Turbulence Model
    Results
Conclusion
Future Plans
References

## Slide 4: Introduction

## Slide 5
Chart: CAFE Requirements per annum
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Fuel Economy Cars | 36 | 37 | 38 | 39 | 41 | 44 | 45 | 47 | 49 | 51 | 53 | 56 | 58 | 60
Requirement from CAFE in the next decade
Extrapolation from the current mileage achieved
Comparing Extrapolation of the current achieved mileage, to the estimated mileage proposed by CAFE

## Slide 6: How Car Manufacturers Control Fuel Economy
Aerodynamics
Weight reduction
  Same performance and safety for less weight
Managing their respective powertrain system
  Monitoring energy consumed/generated
  Looking for alternative systems

## Slide 7: GM’s Alternative Powertrain Vehicles
Chevrolet Volt (2010) and Bolt (Concept shown in 2015 North American International Auto Show)
[3]
[3]

## Slide 8: The Problem!
Plug-in Hybrid Vehicles (PHEV); Hybrid Vehicles (HV); Electrical Vehicles (EV)
  Run out of electrical energy in short ranges PHEV (30-80 km); EV (max ~300 km)
  Higher charging times
PHEV, HV, and EV cars need to have better driving ranges
[3]

## Slide 9: Goal Statement
New mechanical and/or electrical framework needed to improve the driving range for PHEV, HV, and EV cars
  System needs to be self generating (Incorporate sustainable energy)
  Charge battery modules when vehicle in motion and/or stationary

## Slide 10: Constraints
Fit within the space limitation of the car
  Any brand or model
Generate enough energy and power to charge the battery
Use sustainable energy source
Work when automobile is stationary and/or moving

## Slide 11: Criteria
Safety
  Risk to the passengers and operators of vehicle
Performance
  How much energy can we extract?
  How much weight will it add?
Cost
  Manufacturing complexity
  Maintenance and warranty
Knowledge
  How well understood is the performance of the system
  What tools do we need to develop to make system feasible

## Slide 12: Possible Extraction Methods to Harvest Electrical Energy

## Slide 13: Hydrogen Fuel Cell
Exhaust
Pt
Pt
Catalyst
Catalyst
Hydrogen (H2) gas from reservoir
Oxygen air (O2) intake from the air
Proton Exchange Membrane (PEM)
H2  2H+ + 2e-
½O2 + 2H+ + 2e-  H2O

## Slide 14: Solar “voltaic” Cells (SVC)
Photoelectric Effect  light energy into electrical energy
Light – Incident Ray
p
n
Current
Load
e-
e-

## Slide 15: KERS

## Slide 16: Wind Energy
Generator
+
-
Transmission/Gears
Wind (kinetic) energy is converted to electrical energy

## Slide 17
All four designs evaluated based on the criteria given above
Solutions: → |  |  | Hydrogen Fuel Cells |  | Solar "Voltaic" Cells |  | KERS |  | Wind | 
Criteria ↓ | Weight | Weight (%) | # | % | # | % | # | % | # | %
Safety | 10 | 34% | 5 | 17% | 10 | 34% | 8 | 28% | 10 | 34%
Performance | 8 | 28% | 6.5 | 22% | 4 | 14% | 7 | 24% | 6.5 | 22%
Cost | 5 | 17% | 2.5 | 9% | 3 | 10% | 4 | 14% | 5 | 17%
Knowledge Behind the Concept | 6 | 21% | 3 | 10% | 4.5 | 16% | 6 | 21% | 6 | 21%
Total: → | 29 | 100% | 17 | 59% | 21.5 | 74% | 25 | 86% | 27.5 | 95%
1 -> Lowest Concern 10 -> Highest Concern |  |  |  |  |  |  |  |  |  | 

## Slide 18: Feasibility Study
Current power and efficiency of current PHEV, HV, and EV
  Chevrolet Volt: 111kW (149 bhp) @ 80 km range
  Battery Size: 17.1 kWh
Establish our goal for range improvement
  + 30% range = 104km range  + 4.032 kWh of Energy Harvesting
  + 50% range = 120km range  + 7.182 kWh of Energy Harvesting
Determine energy harvesting capability
  What is the maximum energy we can theoretically extract
Determine energy harvesting efficiency
  Mechanical losses (friction, weight increase)
  Thermodynamic losses (entropy)
  Aerodynamic losses (increase in drag)
After all of this, determine if we can ACTUALLY meet our goal of improved range

## Slide 19: Literature Review

## Slide 20: Vertical vs Horizontal Axis Wind Turbine
VAWT
HAWT

## Slide 21: Lift vs Drag Driven turbine

## Slide 22: Efficiency of Different Type of Turbines

## Slide 23: General Theory & Key Concepts
2D – Airfoil Diagram

## Slide 24: General Theory & Key Concept
2D – Airfoil FBD, in an ideal situation with now skin drag

## Slide 25: General Theory & Key Concepts

## Slide 26: General Theory & Key Concepts
Airfoil used
  NREL and NACA are most common airfoil used to design the wind turbine

## Slide 27: Blade Element Momentum (BEM) Theory Assumptions
Momentum Theory
  Blades operate without frictional drag
  A slipstream that is well defined separates the flow passing through the rotor disc from outside disc
  The static pressure in and out of the slipstream far ahead of and behind the rotor are equal to the undisturbed free-stream static pressure (p1 = p3)
  Thrust loading is uniform over the rotor disc
  No rotation is imparted to the flow by the disc
  Based on state flow

## Slide 28: BEM Theory Assumptions
Blade Element
  There is no interference between successive blade elements along the blade
  Forces acting on the blade element are solely due to the lift and drag characteristics of the sectional profile of a blade element

## Slide 29: BEM Theory

## Slide 30: BEM – 2D Element

## Slide 31: BEM – 2D Element

## Slide 32: BEM – 2D Forces

## Slide 33: BEM a & a’ Iteration

## Slide 34: Computational Fluid Dynamics (CFD) - ANSYS

## Slide 35: Gertz Experimental Model
Airfoil Used: N83X series
Number of Blades: 3
Designed Tip Speed Ratio (TSR): 5.4
Rotational Speed: 200 rpm
Radius: 1.65 m
Temperature: 300 K

## Slide 36: NREL S83X series

## Slide 37: Gertz Experimental Model
Gertz chord and pitch varying throughout the blade length

## Slide 38: CFD Fluent Theory Model Assumption
Fluid is Newtonian
There is only one phase present
The problem domain throughout the analysis does not change
The user has to define 2 set of parameter on what type of fluid flow
  Fluid flow is assumed turbulent
  The fluid is assumed incompressible

## Slide 39: CFD Fluent Theory Model Generation
Reynolds (Ensemble) Average
Filtered Navier-Stokes Equation
Hybrid RANS-LES Formulation
Bossinesq Approach vs Reynolds Stress Transport Models

## Slide 40: Fluent Geometry

## Slide 41: Fluent Mesh

## Slide 42: Boundary condition

## Slide 43: Boundary Condition

## Slide 44: Turbulence Model
Transitional SST
  Specially created to monitor airfoil flow
  An upgrade version of k-w SST (k-omega Shear Stress Transport) models with additional 2 transport equations
    k-w SST model is more accurate and reliable for a wider class of flows
      Adverse pressure gradient flows
      Airfoils
      Transonic shock waves

## Slide 45: Solution

## Slide 46: Solution

## Slide 47
Chart: Cp (Coefficient of Power) vs TSR (Tip Speed Ratio)
| 1.5092099999999999 | 1.74613 | 1.9832099999999999 | 2.2414900000000002 | 2.41344 | 2.79914 | 2.9058600000000001 | 3.0557300000000001 | 3.1840299999999999 | 3.4414899999999999 | 3.6562800000000002 | 3.8067600000000001 | 4.1938300000000002 | 4.4951600000000003 | 4.6678300000000004 | 4.9478 | 5.0768599999999999 | 5.3997799999999998 | 5.7666300000000001 | 6.2193800000000001 | 6.4351000000000003 | 6.7156200000000004 | 6.9749400000000001 | 7.2777000000000003 | 7.5805100000000003 | 7.9265499999999998 | 8.3589699999999993 | 8.8351000000000006 | 9.3123199999999997 | 9.8554999999999993 | 10.4618
Cp - Gertz | 0.036709 | 0.048101 | 0.055696 | 0.072152 | 0.088608 | 0.15316 | 0.18101 | 0.20886 | 0.23671 | 0.27215 | 0.2962 | 0.31013 | 0.34304 | 0.36202 | 0.36202 | 0.37595 | 0.38608 | 0.40506 | 0.40633 | 0.41772 | 0.42025 | 0.42152 | 0.41392 | 0.4 | 0.38481 | 0.36835 | 0.35063 | 0.32025 | 0.26456 | 0.18101 | 0.13544
Cp -Simulation | 0.13 | 0.25 | 0.35 | 0.4 | 0.44 | 0.43 | 0.42 | 0.4

## Slide 48: Conclusion

## Slide 49: Conclusion
The model has less percentage error for TSR 5-8 when compared to Gertz’s Model
  Cp of 0.42 is achievable on this airfoil
To get better results
  Better and more structured mesh is needed
  More stricter convergence method is needed

## Slide 50: Future Plans

## Slide 51: Future Plans
Adapt this model for the turbine that is going to be used in the car
Check if the size is feasible
Conduct Lap time simulation to see if the energy is generated

## Slide 52: Questions?

## Slide 53: References
Hydrogen Fuel Cells – PEM
  [1] S. G. Chalk and J. F. Miller, “Key challenges and recent progress in batteries, fuel cells, and hydrogen storage for clean energy systems,” J. Power Sources, vol. 159, no. 1 SPEC. ISS., pp. 73–80, 2006.
  [2] L. M. Das, R. Gulati, and P. K. Gupta, “A comparative evaluation of the performance characteristics of a spark ignition engine using hydrogen and compressed natural gas as alternative fuels,” Int. J. Hydrogen Energy, vol. 25, pp. 783–793, 2000.
  [3] Department of Energy, “Hydrogen Fuel Cells Fact Sheet,” 2006.
  [4] H. C. Now, F. Cell, C. Later, J. Deutch, and N. Series, “Hybrid Cars Now, Fuel Cell Cars Later Author(s): Nurettin Demirdöven and John Deutch Source:,” vol. 305, no. 5686, pp. 974–976, 2015.
  [5] J. M. Ogden, M. M. Steinbugler, and T. G. Kreutz, “Comparison of hydrogen, methanol and gasoline as fuels for fuel cell vehicles: implications for vehicle design and infrastructure development,” J. Power Sources, vol. 79, no. 2, pp. 143–168, 1999.
  [6] S. J. Peighambardoust, S. Rowshanzamir, and M. Amjadi, Review of the proton exchange membranes for fuel cell applications, vol. 35, no. 17. Elsevier Ltd, 2010.
  [7] D. K. Ross, “Hydrogen storage: The major technological barrier to the development of hydrogen fuel cell cars,” Vacuum, vol. 80, no. 10, pp. 1084–1089, 2006.
  [8] L. Schlapbach and A. Züttel, “for Mobile Applications,” vol. 414, no. November, pp. 353–358, 2001.
  [9] Y. Wang, K. S. Chen, J. Mishler, S. C. Cho, and X. C. Adroher, “A review of polymer electrolyte membrane fuel cells: Technology, applications, and needs on fundamental research,” Appl. Energy, vol. 88, no. 4, pp. 981–1007, 2011.
  [10] a. Yilanci, I. Dincer, and H. K. Ozturk, “A review on solar-hydrogen/fuel cell hybrid energy systems for stationary applications,” Prog. Energy Combust. Sci., vol. 35, no. 3, pp. 231–244, 2009.
Solar “Voltaic” Cells
  [1] D. A. R. Barkhouse, O. Gunawan, T. Gokmen, T. K. Todorov, and D. B. Mitzi, “Device characteristics of a 10.1% hydrazine-processed Cu2ZnSn(Se,S)4 solar cell,” Prog. Photovoltaics Res. Appl., vol. 20, no. 1, pp. 6–11, 2012.
  [2] M. S. Dresselhaus and I. L. Thomas, “Alternative energy technologies.,” Nature, vol. 414, no. 6861, pp. 332–337, 2001.
  [3] E. Goffman, “Why Not the Sun ? Advantages of and Problems with Solar Energy,” no. December, pp. 1–16, 2008.
  [4] H. B. Gray, “Powering the planet with solar fuel.,” Nat. Chem., vol. 1, no. 2, p. 112, 2009.
  [5] M. a Green and K. Emery, “Solar Cell Eficiency Tables,” vol. 1, no. September 1992, pp. 25–29, 1993.
  [6] P. In and T. Photovoltaic, “Introduction 1. 1.1.”
  [7] a. Muller, B. Edwards, J. Kirkland, and J. Silcox, “Simulation of thermal diffuse scattering including a detailed phonon dispersion curve,” Ultramicroscopy, vol. 86, no. 3–4, pp. 371–380, 2001.
  [8] B. O’Regan and M. Grätzel, “A low-cost, high-efficiency solar cell based on dye-sensitized colloidal TiO2 films,” Nature, vol. 353, no. 6346, pp. 737–740, 1991.
  [9] B. K. Sovacool, “The intermittency of wind, solar, and renewable electricity generators: Technical barrier or rhetorical excuse?,” Util. Policy, vol. 17, no. 3–4, pp. 288–296, 2009.
KERS
  [1] J. B. Bartolo, H. Zhang, D. Gerada, L. De Lillo, and C. Gerada, “High speed electrical generators, application, materials and design,” Proc. - 2013 IEEE Work. Electr. Mach. Des. Control Diagnosis, WEMDCD 2013, pp. 47–59, 2013.
  [2] Bosch Mobility Solutions, “EN Bosch Regenerative Braking.” 2014.
  [3] Z. C. Z. Chuanwei, B. Z. B. Zhifeng, C. B. C. Binggang, and L. J. L. Jingcheng, “Study on regenerative braking of electric vehicle,” 4th Int. Power Electron. Motion Control Conf. 2004. IPEMC 2004., vol. 2, pp. 836–839, 2004.
  [4] Y. S. Li, Q. L. Zeng, C. L. Wang, and W. Liang, “Research on control strategy for regenerative braking of a plug-in hybrid electric city public bus,” 2009 2nd Int. Conf. Intell. Comput. Technol. Autom. ICICTA 2009, vol. 1, pp. 842–845, 2009.
  [5] D. Parashar, “regenerativebrakingsystem-copy-140322013044-phpapp02,” 2014, pp. 1–34.
  [6] J. W. Post, H. V. M. Hamelers, and C. J. N. Buisman, “Energy recovery from controlled mixing salt and fresh water with a reverse electrodialysis system,” Environ. Sci. Technol., vol. 42, no. 15, pp. 5785–5790, 2008.
  [7] W. Rose, “White Rose Research Online,” Bilingualism, vol. 110, pp. 115–122, 2009.
  [8] “Chassis Systems Control Reduce consumption . Protect the environment . Regenerative braking systems Regenerative braking systems increase range and reduce CO 2 emissions.”
  [9] “2165.” .
Wind
  [1] R. Billinton and G. Bai, “Generating capacity adequacy associated with wind energy,” IEEE Trans. Energy Convers., vol. 19, no. 3, pp. 641–646, 2004.
Mics.
  [1] F. Armani, S. Armani, A. Armani, and R. Hill, “(19) United States (12),” vol. 1, no. 19, p. 17, 2011.
Text goes here

## Slide 54: Visual Aids
[1] F. Felix, “Oil output to hit 500,000 barrels daily.” 2014.
[2] Motertrend, “2013-tesla-model-s-front-1.” 2014.
[3] Electrovelocity, “2011-chevy-volt-front.” 2010.
[4] Newcars, “2012-Nissan-LEAF-Coupe-Hatchback-SV-4dr-Hatchback-Photo-9.” .
[5] D. Parashar, “regenerativebrakingsystem-copy-140322013044-phpapp02,” 2014, pp. 1–34.
[6] R. Dervisgolu, “Solid_oxide_fuel_cell_protonic.” 2012.
[8] T. Dangkhoa, “Solar cell,” Solar Energy. pp. 1–26, 2005.
[9] “1921rpsaxq1zpjpg.” .
[10] Bosch Mobility Solutions, “EN Bosch Regenerative Braking.” 2014.
[11] F. Armani, S. Armani, A. Armani, and R. Hill, “(19) United States (12),” vol. 1, no. 19, p. 17, 2011.
[12] “mitsubishi-imiev-black-6.” .
Text goes here

## Slide 55: Thank You!